Humidify your home in the winter

Source:  Robert Fehr, extension professor, environmental control systems

Winter weather in Kentucky tends to present challenges in the form of snow, ice and freezing temperatures. What isn’t talked about often is the discomfort caused by weather inside the home. The itch that plagues many people during winter can be the result of inside air that does not contain adequate moisture. Low humidity levels can cause high levels of discomfort including dry skin and stuffy sinuses.

The air in a house is dryer in winter because there is less moisture in the air outside.  Outside air at 30 degrees and 100-percent humidity will have humidity of less than 25 percent when warmed up to 70 degrees.  Many newer homes have built-in humidifiers, but commonly they are not maintained and do a poor job.  For less than $30, a simple hygrometer gives an accurate reading of the relative humidity level.

To correct a dry air situation, homeowners should first make sure the heating system duct work is not leaking. A tight duct system saves energy and reduces the amount of outside air coming in the house. Look at both the supplies and the returns in the crawl space, attic or unconditioned basement. Secondly, seal any air leaks around windows, doors, plugs in outside walls, and other openings to the outside. If the house has a gas furnace, check for the presence of an outside air supply directly to the furnace room. This is typical in newer homes, but may not exist in older homes. This outside air supply reduces the amount of outside air brought into the rest of the house. If the furnace is not energy efficient, consider upgrading to a sealed combustion unit. Rated over 90-percent efficient, these units are eligible for state and federal tax credits.

Potential problems can be created when adding moisture to the air in winter. When outside air and inside air contain the same amount of water, typically condensation will not accumulate on windows, non-insulated walls, or other cold surfaces. Raising the amount of water in inside air can create condensation problems on these surfaces.

Humidity should be raised just enough to create a comfortable environment.  Levels of 35 percent or less are adequate in winter.

If you have taken steps to make your home air tight and have properly vented your furnace, but the air is still too dry, try adding some houseplants to your décor. If the problem is most noticeable at night, a small humidifier in the bedroom might do the job.

For more information contact the (COUNTY NAME) Cooperative Extension Service.  Educational programs of the Cooperative Extension Service serve all people regardless of race, color, sex, religion, disability or national origin.

-30-